## Slide 1: Turtlebot3 Pose Controller

## Slide 2: Control Approach
The robot uses a Proportional Controller (P Controller)
In this type of controller, speed is proportional to error.
The further away the goal is, the faster the robot moves.
The closer it gets to the goal, the slower it moves.
Every time the robot moves, gazebo send the position coordinates on ‘/odom’.
The angle is received as a quaternion and it is converted using the formula in the ‘def get odom’ function in the code.

## Slide 3: How Pose Errors Are Calculated
Distance errors: the straight line distance from the robot to the goal is calculated using Pythagoras theorem. (distance = sqrt(dx ** 2 + dy **2))
Heading errors: deals with how much does the robot need to turn to face the goal.
heading_error = self.normalize(angle_to_goal - current_yaw)
Orientation errors: deals with how much the robot needs to rotate to face the right way at the destination.
Orientation_error = goal_yaw - current_yaw
All angles are normalized between -180 and +180
Without normalization, the robot will spin in the wrong way at the destination.

## Slide 4: How Velocity Commands Are Generated
The controller runs in two phases:
Phase 1 - when the distance is more than 5 cm
Forward = 0.5 x distance
Turn = 1.5 x heading_error
Phase 2 - when the distance is less than 5 cm
Forward = 0.0
Turn = 1.5 x orientation_error
Both commands are sent simultaneously making the robot drive and turn at the same time.
For the robot to stop, two conditions must be true:
Distance to goal must be less than 5 cm and the angle error must be less than 5 degrees.

## Slide 5: Assumptions Made
The robot operates on a flat surface only.
There are no obstacles in the path of the robot.
One goal is processed at a time.
Odometry data is without noise.

## Slide 6: Known Limitations
No obstacle avoidance. The robot will collide with any obstacles introduced in its path.
Odometry drifts over long distances so data can become inaccurate.
Final angle corrections can be slow for small errors.